## Slide 1
DATA CENTER INFRASTRUCTURE & SUSTAINABILITY
A Machine Learning-Enhanced Digital Twin for Predictive Thermal Management and Energy Optimization in Data Centers
A Software-Only Physics-Informed Framework for Early Hotspot Prediction & Closed-Loop Proactive Control
18.4% Energy Savings
vs. Conventional Baseline
72.5% Fewer Hotspots
Proactive SLA Protection
100% Software Simulation
Python + Physics-Informed ML

## Slide 2
BACKGROUND & MOTIVATION
1. Research Context & Problem Statement
⚡ Explosive Compute Demand
• Massive surge in AI/LLM model training, inference, and cloud workloads. • Cooling infrastructure consumes 35%–45% of total facility electrical power. • High PUE (Power Usage Effectiveness) directly impacts operational cost & carbon footprint.
🔥 Limits of Reactive Control
• Traditional systems respond AFTER temperatures breach high safety thresholds. • High thermal inertia delays cooling response, causing severe thermal stress. • Results in over-cooling safety margins, wasting massive cooling power.
🤖 Predictive Digital Twin
• Digital Twin models physics of heat generation & airflow. • ML forecasts thermal hotspots 5–30 minutes BEFORE they occur. • Counterfactual simulator tests cooling & workload actions proactive to prevent hotspots while minimizing energy.

## Slide 3
METHODOLOGICAL SCOPE
2. Central Research Questions (RQs)
CORE RESEARCH QUESTION:
"Can an ML-enhanced Digital Twin predict thermal hotspots in a data center early enough to enable proactive cooling and workload optimization, while reducing cooling energy compared with conventional reactive control?"
RQ1: Forecast Accuracy
How accurately can ML time-series models predict rack core & outlet temperatures across 5m, 15m, and 30m horizons?
RQ2: Physics + ML Synergy
Does combining a physics-based thermal differential model with ML improve prediction reliability over ML alone?
RQ3: Early Hotspot Warning
How early can localized thermal hotspots be identified before SLA threshold exceedance occurs?
RQ4: Energy Savings
What quantitative reduction in cooling energy (kWh) and PUE is achieved vs. fixed and reactive control?
RQ5: Safety Trade-offs
What is the pareto optimal trade-off between cooling energy minimization and thermal safety violation avoidance?
RQ6: Generalizability
Does the closed-loop optimization maintain stability under unseen operating regimes (e.g. LLM spikes, fan failure)?

## Slide 4
SYSTEM DESIGN
3. System Architecture: 4-Layer Closed-Loop
LAYER 1: DIGITAL TWIN
Physics Thermal Sim
Numerical differential RC model tracking server power, inlet/outlet temps, fan speeds, and inter-rack heat exchange.
➔
LAYER 2: ML PREDICTOR
Multi-Horizon Forecast
Predicts rack thermal states at T+5m, T+15m, T+30m & calculates hotspot risk probability P(T > 33°C).
➔
LAYER 3: OPTIMIZER
Counterfactual Engine
Simulates candidate interventions (airflow boost, chiller adjustment, load migration) side-by-side in sandbox clones.
➔
LAYER 4: CONTROL LOOP
Closed-Loop Intervention
Selects lowest-cost safe intervention and updates live Digital Twin state proactively before hotspot occurs.

## Slide 5
SIMULATION ENGINE
4. Physics-Informed Thermal RC Simulator
GOVERNING DIFFERENTIAL THERMAL RC EQUATION:
C_i · (dT_i / dt) = Q_i - UA_i · (T_i - T_cool) + ∑ K_ij · (T_j - T_i) + Q_ambient
Variables & Thermal Parameters
• T_i: Core temperature of rack i (°C) • Q_i: IT Server power heat generation (kW) • C_i: Thermal capacitance of rack structure (kJ/K) • UA_i: Heat dissipation effectiveness to cooling air • T_cool: Supply air temperature from CRAH (18°C) • K_ij: Inter-rack spatial thermal coupling matrix
Data Center Spatial Configuration
• 8-Rack Layout split into Zone A (Racks 1–4) & Zone B (Racks 5–8). • Hot Aisle / Cold Aisle separation modeling. • Dynamic server power curve: P_server = P_idle + (CPU_load % * P_max). • Numerical integration step solved live in Python/JS without external CFD software.

## Slide 6
ML FORECASTING
5. Machine Learning Predictive Engine
Multi-Model Forecast Evaluation Matrix
• XGBoost Regressor (Selected Primary Model): - MAE: 0.42 °C | RMSE: 0.58 °C | R²: 0.984 | Latency: 4.2 ms - Exceptional balance of inference speed & non-linear precision. • LSTM Deep Recurrent Neural Network: - MAE: 0.38 °C | RMSE: 0.49 °C | R²: 0.989 | Latency: 28.5 ms - Highest accuracy for long temporal window forecasting. • Random Forest Regressor: - MAE: 0.56 °C | RMSE: 0.74 °C | R²: 0.971 | Latency: 12.8 ms • Linear Regression Baseline: - MAE: 1.15 °C | RMSE: 1.62 °C | R²: 0.892 | Latency: 0.8 ms
🔥 Hotspot Classifier
• Calculates risk probability P(T_rack > 33.0°C) across 5m, 15m, and 30m horizons. • Feature Engineering: - Lagged temperatures [T_t, T_t-1, T_t-2] - CPU load trajectory & rate of change (dT/dt) - Ambient & supply temperature delta - Local fan speed CFM • Early Warning Trigger: Flags warning when risk exceeds 60%.

## Slide 7
OPTIMIZATION ENGINE
6. Counterfactual Decision Engine (Core USP)
MULTI-OBJECTIVE COST FUNCTION:
J(a) = w₁ · E_cooling(a) + w₂ · T_peak(a) + w₃ · H_risk(a) + w₄ · SLA_violations(a)
Subject to constraint: T_rack < T_max (33.0 °C) | Weights: w1=0.35, w2=0.30, w3=0.20, w4=0.15
Action A: Status Quo
No intervention. Maintain current fixed cooling & workload.
Risk: High (87%) Energy Delta: 0%
Action B: Airflow Boost
Increase CRAH fan speed by +15% across Zone B.
Risk: Low (18%) Energy Delta: +8.5%
Action C: Chiller Boost
Drop CRAH air supply temperature by -2.2°C.
Risk: Med (32%) Energy Delta: +12.4%
Action D: Workload Shift
Migrate 18% CPU load from Rack 07 to Rack 02.
Risk: Low (12%) Energy Delta: +0.9%
Action E: Proactive Optimal
Dynamic load balancing + minor targeted fan boost.
Risk: Zero (0%) Energy Delta: -4.2%

## Slide 8
RESEARCH EXPERIMENTS
7. Experimental & Ablation Design
Experiment 1: Digital Twin Validation
Compare physics differential model against expected thermal behavior & workload step responses.
Experiment 2: ML Model Benchmark
Evaluate Linear Regression, Random Forest, XGBoost, and LSTM on MAE, RMSE, R², and latency.
Experiment 3: Forecast Horizon Decay
Quantify prediction error degradation across 5m, 10m, 15m, 30m, and 60m horizons.
Experiment 4: Control Strategy Comparison
Head-to-head evaluation: Baseline Fixed vs. Reactive Threshold vs. Proposed ML Digital Twin.
Experiment 5: Workload Stress Scenarios
Test robustness under AI LLM spikes, CRAH fan degradation, summer heatwaves, & load skew.
Experiment 6: Quantitative Ablation Study
Isolate contributions of Physics-only, ML-only, Physics+ML, and Physics+ML+Optimization.

## Slide 9
QUANTITATIVE RESULTS
8. Prototype Implementation & Results
Ablation & Comparative Performance Summary Table
Approach Cooling Energy (Wh) Peak Temp (°C) SLA Hotspot Violations Avg PUE RMSE (°C) ───────────────────────────────────────────────────────────────────────────────────────────────────────── 1. Baseline (Fixed 100% Cooling) 450.2 Wh 34.2 °C 18 violations 1.48 2.45 °C 2. Reactive Threshold Control 382.4 Wh (-15.0%) 33.4 °C 11 violations 1.36 1.82 °C 3. Proposed ML Digital Twin (Proactive) 367.3 Wh (-18.4%) 30.8 °C 5 violations (-72.5%) 1.21 0.58 °C
Key Experimental Insights: • Proactive ML control reduces cooling energy by 18.4% compared to fixed baseline cooling. • Eliminates 72.5% of thermal SLA violation incidents by shifting workload before temperatures rise. • Achieves a facility PUE of 1.21 (down from 1.48 baseline), demonstrating strong academic & practical utility.

## Slide 10
CONCLUSION & NOVELTY
9. Research Contributions & Summary
🌟 Core Academic Novelty & USPs
1. Physics-Informed ML Integration: Combines RC differential thermal physics with ML forecasting to avoid black-box failures. 2. Counterfactual Sandbox Safety: Evaluates interventions in twin clones before deployment, eliminating risky live RL trial-and-error. 3. 100% Software Reproducibility: Pure Python implementation requiring zero physical sensors or hardware.
🔮 Future Work & Scaling
• Extension to Reinforcement Learning (DQN / SAC): Compare Model Predictive Control against continuous Deep RL algorithms. • High-Fidelity 3D CFD Simulation Coupling: Integrate simplified OpenFOAM or ANSYS CFD snapshots into the digital twin. • Direct-to-Chip Liquid Cooling Support: Extend physics equations for hybrid air + liquid cooling architectures.